## Slide 1: TCP/IP Internetworking II
Chapter 9
Panko and Panko
Business Data Networks and Security, 11th Edition
© 2015 Pearson Education

## Slide 2: Perspective
Chapter (s) | Coverage | Layers
1–4 | Core concepts and principles | All
5 | Single switched networks | 1–2
6–7 | Single wireless networks | 1–2
8–9 | Internets | 3–4
10 | Wide Area Networks | 1-4
11 | Applications | 5

## Slide 3: Perspective
Chapter 8
  Major TCP/IP standards
  Router operation
Chapter 9
  Managing Internets
  Securing Internets

## Slide 4
IP Subnetting
Network Address Translation (NAT)
Domain Name System (DNS)
Simple Network Management Protocol
IP Security (IPsec)
IPv6 Management
Other TCP/IP Supervisory Standards

## Slide 5: 9.1: IPv4 Subnetting
Companies are given network parts by their ISP or an Internet number authority.
They divide the remaining bits between a subnet part and a host part.
Larger subnet parts mean more subnets means but hosts per subnet.
Smaller subnet parts mean fewer subnets but more hosts per subnet.

## Slide 6: 9.1: IPv4 Subnetting
If a part has N bits, it can represent 2N - 2 subnets or hosts per subnet.
  2N because if you have N bits, you can represent 2N possibilities.
  Minus 2 is because you cannot have a part that is all zeros or all ones.
Part Size
(bits)
2N
2N-2
4
24 = 16
16-2 = 14
8
?
?
12
4,096
4,094
65,536
65,534
16
10
?
?

## Slide 7: 9.1: IPv4 Subnetting
Description
Step
32
Total size of IP address
(bits)
1
Size of network part
assigned to firm (bits)
2
16
Remaining bits for firm
to assign
3
16
Selected subnet/host part
sizes (bits)
4
8 / 8
Number of possible
subnets (2N - 2)
254
(28 - 2)
Number of possible hosts
per subnet (2N - 2)
254
(28 - 2)
By definition
Assigned to
the firm
Bits for the
firm to assign
The firm’s
decision

## Slide 8: 9.1: IPv4 Subnetting
Description
Step
32
Total size of IP address
(bits)
1
Size of network part
assigned to firm (bits)
2
16
Remaining bits for firm to
assign
3
16
Selected subnet/host part
sizes (bits)
4
6/10
Number of possible
subnets (2N - 2)
62
(26 - 2)
Number of possible hosts
per subnet (2N - 2)
1,022
(210 - 2)
By definition
Assigned to
the firm
Bits for the
firm to assign
The firm’s
decision

## Slide 9: 9.1: IPv4 Subnetting
Description
Step
32
Total size of IP address
(bits)
1
Size of network part
assigned to firm (bits)
2
8
Remaining bits for firm to
assign
3
24
Selected subnet/host part
sizes (bits)
4
12/12
Number of possible
subnets (2N - 2)
4,094
(212 - 2)
Number of possible hosts
per subnet (2N - 2)
4,094
(212 - 2)
By definition
Assigned to
the firm
Bits for the
firm to assign
The firm’s
decision

## Slide 10: 9.1: IPv4 Subnetting
Description
Step
32
Total size of IP address
(bits)
1
Size of network part
assigned to firm (bits)
2
8
Remaining bits for firm to
assign
3
24
Selected subnet/host part
sizes (bits)
4
8/16
Number of possible
subnets (2N - 2)
254
(28 - 2)
Number of possible hosts
per subnet (2N - 2)
65,534
(216 - 2)
By definition
Assigned to
the firm
Bits for the
firm to assign
The firm’s
decision

## Slide 11: 9.1: IPv4 Subnetting
Description
Step
Size of network part
assigned to firm (bits)
2
20
Remaining bits for firm to
assign
3
12
Host part size (bits)
4
?
Number of possible
subnets (2N - 2)
?
Number of possible hosts
per subnet (2N - 2)
?
Selected subnet part
size (bits)
Added
4
Size of IP address
2
32
Exercise

## Slide 12: 9.1: IPv4 Subnetting
Description
Step
Size of network part
assigned to firm (bits)
2
20
Remaining bits for firm to
assign
3
12
Host part size (bits)
4
?
Number of possible
subnets (2N - 2)
?
Number of possible hosts
per subnet (2N - 2)
?
Selected subnet part
size (bits)
Added
6
Size of IP address
2
32
Exercise

## Slide 13
IP Subnetting
Network Address Translation (NAT)
Domain Name System (DNS)
Simple Network Management Protocol
IP Security (IPsec)
IPv6 Management
Other TCP/IP Supervisory Standards

## Slide 14: 9.2: Network Address Translation (NAT)
NAT
  Sends packets with false external source IP addresses and port numbers that are different from internal source IP addresses and port numbers
  To expand the number of IP addresses inside the firm
  For security purposes

## Slide 15: 9.3: NAT Operation
NAT Firewall puts the real source IP address and port number in the table.

## Slide 16: 9.3: NAT Operation
NAT Firewall replaces the source IP address and port number of the packet with a false source IP address and port number.
Adds to table.

## Slide 17: 9.3: NAT Operation
NAT Firewall reverses the process for incoming packets.

## Slide 18: 9.3: NAT Operation
NAT Firewall reverses the process for incoming packets.

## Slide 19: 9.2: Network Address Translation
Security Reasons for Using NAT
  External attackers can put sniffers outside the corporation.
  Sniffers read IP addresses and port numbers.
  Attackers can send attacks to these addresses and port numbers.
  With NAT, attackers learn only false external IP addresses. Cannot use this information to attack internal hosts.
Notes: Like in magic, where they can’t hurt you unless they know your true name.

## Slide 20: 9.2: NAT
Expanding the Number of Available IP Addresses
  Companies receive a limited number of IP addresses from their ISPs.
  There are roughly 4,000 possible ephemeral port numbers for each client IP address.
  So for each IP address, there can be up to about 4,000 external connections.
  If a firm is given 248 IP addresses, there can be roughly one million external connections (254 x 4000) IP addresses

## Slide 21: 9.2: NAT
Companies often use private IP addresses internally.
These can be used only within companies—never on the Internet.
There are three Private IP address ranges.
  10.x.x.x
  172.16.x.x through 172.31.x.x
  192.168.x.x (most popular)

## Slide 22
IP Subnetting
Network Address Translation (NAT)
Domain Name System (DNS)
Simple Network Management Protocol
IP Security (IPsec)
IPv6 Management
Other TCP/IP Supervisory Standards

## Slide 23: The Domain Name System (DNS)
A domain is any group of resources (routers, single networks, hosts, etc.) under the control of an organization.

## Slide 24: 9.4: Domain Name System (DNS) Lookup
Originating host needs the IP address of host dakine.pukanui.com.
Asks its local DNS server at Hawaii.edu.

## Slide 25: 9.4: Domain Name System (DNS) Lookup
Host name is dakine.pukanui.com

## Slide 26: 9.4: Domain Name System (DNS) Lookup
Sends response to local DNS server, not the client host.

## Slide 27: 9.4: Domain Name System (DNS) Lookup
Note that the local DNS server always sends back the response message.

## Slide 28: 9.5: Domain Name System (DNS) Hierarchy
The DNS really is a general naming system for the Internet.
A domain is a set of resources under the control of an organization.
There is a hierarchy of domains.

## Slide 29: 9.5: Domain Name System (DNS) Hierarchy
The root is all domains.
There are 13 DNS root servers.

## Slide 30: 9.5: Domain Name System (DNS) Hierarchy
There are two kinds of top-level domains.
Generic top-level domains indicate organization type (.com, .edu, .gov, etc.).
Country top-level domains are specific to a country (.au, .ie, .ch, etc.).

## Slide 31: 9.5: Domain Name System (DNS) Hierarchy
Traditionally, generic top-level domains were strongly limited in number.
There have been a few additions over the year, such as .museum, .name, and .co.
Since 2012, any individual or company can propose to administer a generic top-level domain.

## Slide 32: 9.5: Domain Name System (DNS) Hierarchy
Companies want second-level domain names.
(Microsoft.com, apple.com, panko.com, etc.).
Competition for these names is fierce.

## Slide 33: 9.5: Domain Name System (DNS) Hierarchy
Most companies further divide their organizations into subdomains or subnets.

## Slide 34: 9.5: Domain Name System (DNS) Hierarchy
At the bottom of the hierarchy are individual hosts.

## Slide 35
IP Subnetting
Network Address Translation (NAT)
Domain Name System (DNS)
Simple Network Management Protocol
IP Security (IPsec)
IPv6 Management
Other TCP/IP Supervisory Standards

## Slide 36: 9.6: Simple Network Management Protocol (SNMP)
Core Elements (from Chapter 4)
  Management information base (MIB).
  Stores the retrieved information.
  “MIB” can refer to either the database on the manager or to the database schema.
Manager
MIB

## Slide 37: 9.6: Simple Network Management Protocol (SNMP)
Objects (Figure 9-7)
  Specific pieces of information
  Number of rows in the routing table
  Number of discards caused by lack of resources (indicates a need for an upgrade)
Objects are NOT managed devices!
Objects are specific pieces of data about a managed device.

## Slide 38: Hierarchical SNMP MIB for Routers
System
Objects
(1/system)
IP, TCP, UDP, ICMP Objects
(1/system)
IP, TCP, UDP, ICMP Objects
(1/system)
IP, TCP, UDP, ICMP Objects
(1/system)
Interface Objects
(1/interface)
Interface Objects
(1/interface)
Interface Objects
(1/interface)
System Objects:
System Name,
System Uptime
(since last reboot),
…
IP Objects:
Forwarding.
Row Discards,
Errors,
…
Interface Objects:
Speed,
Up/Down/Testing,
…
System: Router XYZ

## Slide 39
IP Subnetting
Network Address Translation (NAT)
Domain Name System (DNS)
Simple Network Management Protocol
IP Security (IPsec)
IPv6 Management
Other TCP/IP Supervisory Standards

## Slide 40: VPNs
Virtual Private Networks
  Really, just cryptographically protected communication over an untrusted network
  The Internet
  Wireless networks
Private in the sense that no one else can see message contents
We saw host-to-host VPNs in Chapters 3 and 7

## Slide 41: 9.8: VPNs
There are two types of VPN:
Remote access VPNs connect a remote user to a corporate site.
The user connects to a VPN gateway at the site.
Copyright © 2015 Pearson Education, Inc.

## Slide 42: 9.8: VPNs
There are two types of VPNs:
Site-to-site VPNs protect all traffic
traveling between two sites.
Each site has a gateway to encrypt outgoing traffic and decrypt incoming traffic.
Copyright © 2015 Pearson Education, Inc.

## Slide 43: IPsec VPNs
Governed by the IPsec protocols
  Operate at the internet layer
  Automatically protect transport header, application content, and some IP header content.
  Protection is transparent. Upper-level content does not even know that it is being protected
App Content
TCP Header
IP Header
Confidentiality, Authentication, Message Integrity
Copyright © 2015 Pearson Education, Inc.
Tunneling

## Slide 44: 9.10: IPsec Security Associations and Policy Servers
Tunnel Mode?
IPsec gateway

## Slide 45: 9.10: IPsec Security Associations and Policy Servers

## Slide 46: 9.11 IPsec vs. SSL/TLS VPNs
Characteristics of | IPsec | SSL/TLS
Standards Organization | IETF | IETF (created by Netscape as SSL, renamed TLS by the IETF)
Layer | Layer 3 | Layer 4
Built into Browsers, Webservers, and Mail Servers, So Protects These Applications at Little or No Cost | No | Yes

## Slide 47: 9.11 IPsec vs. SSL/TLS VPNs
Characteristic | IPsec | SSL/TLS
Can protect any application | Yes (also protects transport-layer header and some of the IP header) | No (Only SSL/TLS-aware applications such as web and e-mail)
Type of VPNs Supported in the Standard | Host-to-Host Remote Site Access Site-to-Site | Host-to-Host

## Slide 48: 9.11 IPsec vs. SSL/TLS VPNs
Characteristic | IPsec | SSL/TLS
Strength of Security | Excellent | Good
Security can be Managed Centrally | Yes | No
IETF’s Security Plan:
Implement IPsec for all transmissions.
Automatic message security for the transport and application layers

## Slide 49
IP Subnetting
Network Address Translation (NAT)
Domain Name System (DNS)
Simple Network Management Protocol
IP Security (IPsec)
IPv6 Management
Other TCP/IP Supervisory Standards

## Slide 50: 9.12 Internet Layer Protocol Stacks
Application
Transport
IPv4 Only
Single Network
Initially, hosts only had an IPv4 protocol stack
Only knew how to communicate via IPv4
Only had IPv4 addresses
Like everybody speaking the same language.
Notes: Imagine switching to a new language. Initially, everyone only speaks one language.

## Slide 51: 9.12 Internet Layer Protocol Stacks
Application
Transport
IPv4
IPv6
Single Network
The IETF assumed that vendors would create dual-stack hosts.
Dual-stack hosts have both types of IP addresses and speak both versions of IP
Dual-stack hosts could talk to any host using either version of IP
IPv4-only hosts could still communicate with everyone.
Eventually, IPv4 would fade away.
Notes: Like everyone begins to learn a second language.
People who speak the new language use it. Others use the old language.

## Slide 52: 9.12 Internet Layer Protocol Stacks
Application
Transport
IPv6 Only
Single Network
But ran out of IPv4 addresses.
Many new devices only have IPv6 addresses and an IPv6 stack.
Companies must support these new IPv6-only clients.
Server hosts must be dual-stack hosts, or translation is needed
Notes: Now, people are arriving in the country who only speak the new language.
Cannot speak to people who have not learned the new language.

## Slide 53: 9.12 Internet Layer Protocol Stacks
Application
Transport
IPv6 Only
Single Network
Most network management and security tools are mature for IPv4 and can deal with most IPv4 issues.
Most network management and security tools are less able to deal with IPv6.
New. Not in the Book.
Notes: Now, people are arriving in the country who only speak the new language.
Cannot speak to people who have not learned the new language.

## Slide 54: 9.13: Global Unicast Addresses in IPv6
Global Routing Prefix
(network part in IPv4)
Subnet ID
(subnet part in IPv4)
Interface ID
(host part in IPv4)
(Almost)
Always 64 bits
Interface ID is not of variable length like IPv4 host parts.
“Wastes” 64 bits, but there are plenty of bits left.

## Slide 55: 9.13: Global Unicast Addresses in IPv6
Global Routing Prefix
(network part in IPv4)
Subnet ID
(subnet part in IPv4
Interface ID
(host part in IPv4)
(Almost)
Always 64 bits
m bits
n bits
64 bits
m + n = 64

## Slide 56: 9.13 IPv6 Subnetting
Must deal with global IPv6 unicast addresses
  Like public IPv6 addresses
  Have 3 parts but different names
IPv4 | IPv6 | IPv4 Part Length | IPv6 Part Length
Network Part | Routing Prefix | Variable | Variable
Subnet Part | Subnet ID | Variable | Variable
Host Part | Interface ID | Variable | 64 bits
32 bits | Total | 32 bits | 128 bits

## Slide 57: 9.14: 64-Bit Unicast Interface ID
Modified 64-bit Extended Unique Identifier (EUI) Format
First, display the EUI-48 address in hexadecimal notation (48 bits)
  Remove dashes
  Convert text to lower case
AD-B1-C2-D3-E5-F5
adb1c2d3e5f5

## Slide 58: 9.14: 64-Bit Unicast Interface ID
Second, divide the address in half
Insert fffe in the middle
This creates a 64-bit address
adb1c2 fffe d3e5f5
adb1c2fffed3e5f5

## Slide 59: 9.14: 64-Bit Unicast Interface ID
Third, in the first byte (e.g.: 10001101)
Invert the second bit from the right (10001111)
This is called Modified 64-bit EUI
adb1c2fffed3e5f5
afb1c2fffed3e5f5

## Slide 60: 9.14: 64-Bit Interface ID Recap
1. Begin with EUI-48 in hexadecimal notation
2. Remove dashes and make lower case
2. Divide the 48 bits into 2 halves of 24 bits
3. Insert fffe between the two halves
4. Flip the second-least significant bit in the first octet (origin of the “Modified”)
5. Place in 4-hex groups separated by colons

## Slide 61: Other IPv6 Standards
Domain Name System (DNS)
  The DNS information for a host is contained in several records.
  DNS A Record. The A record contains the IPv4 address for the target host name.
  DNS AAAA Record. For IPv6 addresses, a new address record had to be added for each host name.
    IPv6 addresses are four times as long as IPv4 addresses, so the added record is called the AAAA record.

## Slide 62
IP Subnetting
Network Address Translation (NAT)
Domain Name System (DNS)
Simple Network Management Protocol
IP Security (IPsec)
IPv6 Management
Other TCP/IP Supervisory Standards

## Slide 63: Dynamic Routing Protocols
How do routers get their routing tables?
  They constantly exchange information
  Communication must be standardized by dynamic routing protocol
  There are several dynamic routing Protocols
Router
Router
Routing Table
Information
Dynamic
Routing Protocol

## Slide 64: 8.15: Dynamic Routing Protocols

## Slide 65: 8.15: Dynamic Routing Protocols

## Slide 66: 8.16: Dynamic Routing Protocols
Dynamic Routing Protocol | Interior or Exterior Routing Protocol? | Remarks
OSPF (Open Shortest Path First) | Interior | IETF standard. For large autonomous systems that only use TCP/IP.
EIGRP (Enhanced Interior Gateway Routing Protocol) | Interior | Proprietary Cisco protocol. Not limited to TCP/IP routing. Also handles IPX/SPX, SNA, etc.

## Slide 67: 8.16: Dynamic Routing Protocols
Dynamic Routing Protocol | Interior or Exterior Routing Protocol? | Remarks
BGP (Border Gateway Protocol) | Exterior | Organization cannot choose what exterior routing protocol it will use

## Slide 68: Internet Control Message Protocol
ICMP
  To handle supervisory communication between internet layer processes on different hosts or routers
  Avoids making IP handle this type of message
  Standardized by the Internet Control Message Protocol

## Slide 69: 9.17: Internet Control Message Protocol
ICMP provides error advisement messages
Helps in the diagnosis of errors
Does not bring reliability

## Slide 70: 9.17: Internet Control Message Protocol
Ping tells the pinger that the pingee is available.
It also gives round-trip latency

## Slide 71: 9.17: Internet Control Message Protocol